## Slide 2
Hardware
Arduino Uno

## Slide 3: Powering & Programming the Arduino

## Slide 4: USB-Type B Port

## Slide 5: Digital Pins
Digital Signal
1 or 0
HIGH or LOW
5V or 0V
Example: A Light Switch

## Slide 6: Analog Pins
Analog Signal
Varies
0V to 5V
Example: A Volume Knob

## Slide 7: Power Pins
Provide and Receive
5V or 3.3V
Vin = Receive Power
GND = Ground
GND Rules!!
Arduino must always be grounded to any circuit that it is connected to

## Slide 8: Powering the Arduino
Input Voltage
7-12 Volts Recommended
WARNING!!
Do not connect backwards

## Slide 9: Powering the Arduino
Input Power
Barrel Jack

## Slide 10: Power Supply
AC Adaptor
7-12 Volts Recommended
At least 250 milliAmps (mA)
WARNING!!
Plug must be center positive!!

## Slide 11: Powering the Arduino

## Slide 12: Software
Arduino IDE

## Slide 13: Blank Sketch

## Slide 14: Find BareMinimum
File>Example>01.Basics>BareMinimum

## Slide 15: BareMinimum
void setup ()
  Commands and variable declarations that need to be executed only once
Void loop ()
  Commands and/or variable declarations that are constantly update

## Slide 16: Find AnalogReadSerial
File>Examples>01.Basics>AnalogReadSerial

## Slide 17: AnalogReadSerial
int x, y, josie
Serial.begin ()
analogRead ()
Serial.print ()
delay()

## Slide 18: Resources

## Slide 19: Learning>Reference

## Slide 20: Commonly Used Commands